TF6225

1．POW  Power interface

| Pin | Definition |
| --- | --- |
| 1 | +24V, Positive power supply |
| 2 | GND, Negative power |

- OUT   Out interface

| Pin | Definition |
| --- | --- |
| 1 | GND, Power ground(OUT) |
| 2 | OUT1, Blowing signal(The whole process of blowing) The machine is idle, the motherboard output OUT1 low； The machine is working, the motherboard output OUT1 is high。 |
| 3 | OUT2, Blowing signal(The whole process of blowing) it is O2 The machine is idle, the motherboard output OUT2 low； The machine is working, the motherboard output OUT2 is high |
| 4 | OUT3, Blowing signal(The whole process of blowing) , it is N2 The machine is idle, the motherboard output OUT3 low； The machine is working, the motherboard output OUT3 is high |

3.OUT Out interface

| Pin | Definition |
| --- | --- |
| 1 | GND, Power ground(OUT) |
| 2 | OUT4, Output signal (reservations) |
| 3 | OUT5, Output signal (reservations) |
| 4 | OUT6, Output signal (reservations) |
| 2 | OUT7, Output signal (reservations) |
| 3 | OUT8, Output signal (reservations) |
| 4 | OUT9, Output signal (reservations) |

4.Laser   Laser  interface

| Pin | Definition |
| --- | --- |
| 1 | GND, Power ground(OUT) |
| 2 | TTL+(24V) Laser switch signal |
| 3 | TTL-(24V) Laser switch signal |
| 4 | PWM(24V), Laser power |
| 5 | Laser-DA(10V) |

5.Laser   Laser  interface

| Pin | Definition |
| --- | --- |
| 1 | GND, Power ground(OUT) |
| 2 | TTL+(5V) Laser switch signal |
| 3 | TTL-(5V) Laser switch signal |
| 4 | PWM(5V), Laser power |
| 5 | Pressure-DA(10V) |

The laser interfaces with the the universal laser power connection as shown below

6.X/Y/Z/U axis interface

| Pin | Definition |
| --- | --- |
| 1 | DC5V, Power(OUT) |
| 2 | PUL, Pulse signal |
| 3 | DIR, Direction signals |

The interface with the drive connected as shown below:

7.X / Y limit interface

| Pin | Definition |
| --- | --- |
| 1 | GND Power ground(OUT) |
| 2 | ELX-; The lower limit of the X-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal.。 |
| 3 | ELY-; The lower limit of the Y-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal |
| 4 | ELX+; the upper limit of X_axis the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 5 | ELY+; the upper limit of Y_axis the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 6 | DC24V, Power(OUT), |

8.Z/U limit interface

| Pin | Definition |
| --- | --- |
| 1 | GND Power ground(OUT) |
| 2 | ELZ- The lower limit of the Z-axis,the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal.。 |
| 3 | ELZ+ the upper limit of Z_is the axis movement to the sensor signal input signal at the maximum coordinate limit |
| 4 | ELV-; The lower limit of the V-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal. |
| 5 | ELW-; The lower limit of the W-axis, the axis movement to a minimum at the coordinate (zero position) limit sensor signal input signal. |
| 6 | DC24V, Power(OUT) PROTECT, Water protection input signal |

8.IN  put interface

| Pin | Definition |
| --- | --- |
| 1 | Power(OUT) GND Power ground(OUT) |
| 2 | IN1, Cap protection signal (input), active low |
| 3 | IN2, The footswitch signal (input), active low |
| 4 | IN3 |
| 5 | IN4 |
| 6 | DC24V, |

9.IN  input interface

| Pin | Definition |
| --- | --- |
| 1 | Power(OUT) |
| 2 | IN5, Water protection input signal |
| 3 | 1N6, Input signal (reserved) |
| 4 | 1N7, Input signal (reserved) |
| 5 | 1N8, Input signal (reserved) |
| 6 | DC24V, |